## Slide 1
10/15
Completed:
Checked the system person by person against my own hand-made list of who really passed
  4 clips (2 day, 2 night), 21 people. “Found” = counted AND correctly called cyclist or pedestrian, so wrong totals can no longer cancel out
Improved it: 6 of 21 people found → 19 of 21
  Three fixes: look at small image tiles (SAHI), combine several opinions before labelling (fusion), and a night-time exception for short sightings
Removed false counts: a barricade that never moves was counted as 2 pedestrians at night → now 0
Looked at the 2025 camera: it is a fisheye (very wide, curved lens), so the system does not work well on it as-is
Redrew the Colonial zone outlines (the bike lane was wrong); still need to check them on a real frame
Wrote a plain-English guide to every technical term (slide 2 and the last slide)

## Slide 2
How the System Works, in Plain English
Step | What it does | Why it matters
1. Detector (RT-DETR) | Looks at every video frame and draws a box around each person and vehicle | Trained by me on ~200 labelled images: it knows person, cyclist, car, truck, bus, other vehicle
2. Tiles (SAHI) | Also looks at 8 overlapping close-up tiles of each frame, plus the whole frame | Far-away people are tiny; zooming in lets the detector see them
3. Tracker (ByteTrack) | ByteTrack links the boxes of one person across frames into a single “track”; I added a step that rejoins a track after a short gap | So each person is counted once, not once per frame
4. Video classifier (X-CLIP) | Watches a track for a few seconds and decides: cyclist or pedestrian | A video model sees motion (pedalling vs walking), not just one picture
5. Fusion | Final label = three opinions combined: the video classifier, the detector’s guess in each frame, and the person’s speed | One model alone makes mistakes; when they disagree, fixed if-then rules decide (next slide)
6. Counting rules | Count a track only if on screen 3 s (night exception), and ignore things that never move | Stops flickers and objects like a barricade being counted as people
Pedestrians on the grass are not excluded: the zone outlines only remove vehicles; people are never removed by them.

## Slide 3
Fusion: Exactly How the Final Label Is Decided
Step | Rule (fixed numbers I set by hand) | In words
Start | Label = X-CLIP’s more likely class for the track (answers averaged over the track, closer and larger views count more) | The video classifier gets the first say
1. Veto | IF X-CLIP = bicyclist AND the detector said “cyclist” in < 15% of the track’s frames → pedestrian | The detector almost never saw a cyclist shape, so overrule
2. Speed | Only if moving left/right and seen ≥ 1.5 s: IF speed < 0.8 AND detector “cyclist” < 50% → pedestrian; IF speed > 2.0 AND detector “cyclist” ≥ 50% → bicyclist | Slow = walking, fast = riding, but only when the detector agrees with the speed
3. Night short sightings | IF 21:00-06:00 AND on screen 0.3-3 s AND detector “cyclist” ≥ 90% AND X-CLIP bicyclist ≥ 90% → count as bicyclist | Dark riders are often tracked for under 3 s
4. Count filter | Count only if on screen ≥ 3 s (except step 3) AND not still: moved < 5 px in total and slower than 0.05 body heights/s = ignored | No flickers, no barricades
There is no single equation and nothing is trained: these are if-then rules with fixed thresholds. Detector “cyclist” % = share of the track’s frames where the detector’s own label was cyclist, not person. A fifth rule (“promote”) was never right and is switched off.

## Slide 4
Speed: How It Is Measured and Whether It Helped
How I measure it
  Follow the person’s feet (bottom-centre of the box, smoothed). Sideways pixels moved per second ÷ box height in pixels = “body heights per second”
  Dividing by height roughly cancels distance: far people move fewer pixels but are also smaller. Walking limit 0.8, riding limit 2.0 (estimated by hand; a simulated 1.4 m/s walker ≈ 0.8, a 5 m/s rider ≈ 2.9)
  Only left/right movement is used: people walking toward or away from the camera look slow even when they are not
Did it help? (21 people; tracks whose label the rule changed)
  Speed rule at 0.8 / 2.0: changed 4 tracks, all 4 correct (1 night cyclist rescued, 3 pedestrians fixed). Detector veto: changed 3, all 3 correct
  An earlier limit of 1.0 wrongly flipped 2 real cyclists, so I use 0.8. Thresholds were set on the two first clips; 1 of the speed fixes (12:45) was on a clip not used for setting
  Not yet proven: the veto and speed overlap on some people, and I never re-ran without speed. That test (“ablation”) is queued: 4 clips, speed off vs on
Not the standard way yet: the standard is to calibrate the camera, convert pixels to metres on the road, and get real km/h. I have not done that or checked my speeds against the speed Excel files

## Slide 5
Results: People Found on 4 Hand-Labelled Clips
Clip (people in my list) | Before changes | + Tiles (SAHI) | + Fusion + night rule | + Ignore still objects (current best)
Night 21:15-21:30 (6) | 0 | 2 | 4 | 4
Day 14:00-14:15 (5) | 3 | 3 | 5 | 5
Night 22:00-22:15, not used to set rules (5) | 0 | 5 | 5 (+2 false counts) | 5 (0 false counts)
Day 12:45-13:00, not used to set rules (5) | 3 | 3 | 5 | 5
Total (21) | 6 | 13 | 19 | 19
Found = the person was counted and called the right thing (cyclist or pedestrian). My list = people I wrote down by watching each clip.
  Still wrong (2 of 21): a night pedestrian called a cyclist, and a night rider visible for only 2.4 s (under the 3 s minimum, not rescued by the night exception)
  Two clips were not used to set the rules (a fair test); the other two partly were
  Early evidence only: one camera, one day, 21 people, and I have watched all four clips. Next: one 15-minute video from each of 2022-2025

## Slide 6
What Changed (and What Did Not Help)
Change | In plain English | Result
Tiles (SAHI) | Cut each frame into 8 overlapping close-ups (plus the whole frame) so tiny far-away people are big enough to detect | 6 → 13 of 21 found
Fusion | Combine 3 opinions: (a) video classifier says cyclist but the detector saw a cyclist shape in under 15% of frames → call it pedestrian; (b) walking is slow and riding is fast: speed is measured in body heights per second | With the night rule: 13 → 19 of 21
Night exception | By day a person must be on screen 3 s. At night, 0.3-3 s still counts as a cyclist if the detector said cyclist in 90%+ of frames and the classifier was 90%+ sure | Finds night riders without adding false day cyclists (a flat 0.4 s rule would have added up to 5 at 14:00)
Ignore still objects | Skip anything that hardly moves (under 5 pixels in total): a barricade | False counts 2 → 0
Tried, no gain (so far)
  Brightening dark night frames (3 methods) before detection: no gain on the 1 night clip I tested; could be retried more carefully
  Lower detector confidence at night; looser tracking; motion blobs; adding 400 outside night images (made the detector worse)

## Slide 7
2025 Video (Fisheye) and Zone Outlines
2025 camera: ran a 15-minute clip and watched it: not good
  Fisheye = very wide curved lens. Cars directly below the camera are not detected; farther objects are
  My detector and settings were made for the flat 2019 camera, so this is not a fair comparison; not scored (no hand list)
Next step: write a tool to flatten (“undistort”) the video. Done: the tool is written; still to do: try it and re-test
  Limit: a flat view cannot show what is straight below the lens, so some loss is unavoidable. Other options: train on fisheye images, or report it as a limitation
Zone outlines (road, bike lane, sidewalk): new bike-lane outline drawn; check on a real frame
  Zones only remove vehicles outside the road and split people into bike lane vs sidewalk. They never remove people, so a pedestrian on the grass is still counted

## Slide 8
Last Week's To-Do: What Is Done and What Is Pending
To-do from 10/6 | Status | What happened
Hand-label ~40 tracks for per-person accuracy | Partly | My list for 21 people on 4 clips is done. The 45-track list (which model is right per person) is still empty
Fusion + speed | Done | Combining opinions and walking-vs-riding speed are in the best setup
More night images to fine-tune | Later | Future work: outside night images made it worse; my own night images come later
Try some techniques | Done | Tiles helped most; brightening and motion blobs gave nothing so far
Analyze both-wrong / one-right cases | Done | Replayed the rules on every person and false count to set the rules
Look at the 2025 cameras | Done | Fisheye, so not a fair comparison
3 s vs shorter, tracking, another site | Partly | Night-only exception (0.3-3 s, strict conditions); tracking no change; no other site yet
Very high sensitivity + review 12 min instead of 60 | Not started | Tool is written, not tried
Why people walking away are missed | Not isolated | Day 14:00 went 3 → 5 of 5 only after fusion; cause not studied directly
Scale to 24 h (~46 GPU-h), then 48 h | Later | Future work, after the new clips confirm the gains

## Slide 9
Literature Enhancements: Which Ones I Implemented
Idea from the literature (plain English) | Status | Outcome
Look at image tiles so small things are seen: SAHI (Akyon, ICIP 2022); AI City Challenge (CVPR 2024) | Implemented | Alone: 6 → 13 of 21 found. Part of the best setup
Combine the label, the detector and the speed (Zangenehpour et al., 2015) | Implemented | Together with the night rule: 13 → 19 of 21
Brighten dark images before detecting (DCExYOLO) | Tried, no gain | Only simple brightening (gamma, CLAHE, Zero-DCE) on one night clip, detector input only. Not DCExYOLO itself. Could retry
Train the detector on hard cases from this camera | Later | Outside night images made it worse. Own images: future work
Use several video frames at once to detect (Corsel WACV 2023; van Lier WACV 2025; FAIM WACV 2025) | Not implemented | Only a simple “what moved” check, no gain. No video-aware detector yet
Night-specific detector (BNE-DETR) | Not implemented | Only if misses remain after the steps above
Takeaway: the cheap, no-training ideas are done. What is left needs new labelled images and new code.

## Slide 10
To Do: Run Next (Code Written, Not Yet Run)
# | To do | Code | How to test
1 | Measure what speed and the veto really add | Written: re-run the best setup with speed off, and with the veto off | 4 labelled clips: people found with vs without each rule
2 | Retry brightening properly | Written: brighten dark frames for the detector AND the video classifier, together with SAHI | 2 night clips with my list: gamma, CLAHE, Zero-DCE vs none
3 | One video each from 2022, 2023, 2024, 2025 | Written: scans each video, records its resolution, picks the 15 min with the most people | I label people in each window; score; no Colonial zone outlines reused
4 | Fisheye 2025: flatten and re-run | Written: choose settings by eye on one frame, convert the clip, re-run | Compare with my list for the clip; else report as a limitation
5 | Per-track accuracy | Tool written; label ~40 tracks | Video classifier vs detector vs combination, per person
6 | Check new zone outlines | None | Overlay image on a real frame
Later (future work): train the detector on my own labelled images; run the full 24 h and 48 h.

## Slide 11
To Do: Ideas I Still Need to Decide On
Idea | Why | Status
Notice when something new enters a still scene | Some people are missed (e.g. a person under an umbrella with the face hidden). Compare each frame with the empty background; wherever something new appears, zoom in and re-check it | A first version (frame differences) found far too many blobs. Needs filtering; not built yet
Night-specific detector (BNE-DETR) | Built for dark scenes | Not built: no ready-made version found; re-implementing from the paper is a research-size task
Check my speeds against the speed Excel files | Shows whether the speed numbers are accurate | Need the Excel file contents; the pixel-to-metre conversion (camera calibration) is also missing
Fix the 2 remaining errors | Night pedestrian called a cyclist; 2.4 s night rider missed | Only judge on new videos, not the clips they came from
Human review of uncertain cases | Catch missed people cheaply | Tool written, not tried

## Slide 12
Plain-English Glossary
Term | Meaning
Detector / RT-DETR | The AI that draws boxes around people and vehicles in a picture
Fine-tuned | Taking a ready-made AI and giving it extra training on my own labelled images
X-CLIP | A video AI that watches a few seconds of a track and says cyclist or pedestrian
Track | One person followed from frame to frame
SAHI | Detecting on small zoomed-in tiles of the frame so tiny people are seen
Fusion | Final label from several opinions (video AI, detector, speed), not one
False count / false track | Counted as a person but nobody was there (e.g. a barricade)
Not used to set rules | Clips I did not use to choose the rules, so the test is fair
Fisheye / undistort | Very wide curved lens / flattening the picture so lines look straight
ByteTrack | The tracking method that links a person’s boxes from frame to frame
Ablation | Switching one rule off and re-running, to measure what that rule really adds
GPU-hour | One hour of one graphics processor on the university cluster